## Slide 1: Smart Bookstand
Project Design

## Slide 2: Ideas behind the “Smart Bookstand”
“Your reading experience should be more than a simple woodblock”
“No bookstand has a decent lighting system embedded within”
“Why can’t bookstands be portable?”

## Slide 3: Overview <Fritzing>

## Slide 4: Overview <KiCAD>

## Slide 5: Overview KiCAD PCB Design

## Slide 6: Lighting system - Fritzing
RGB LEDs – 8 of them
Each with a current limiting resistor
Red -> connected using 470Ω
Green / Blue -> 1kΩ
74HC595 Shift Register
One for each color – 3 total
8 outputs connected to each LED
Will be connected to SPI1, 3CEs
I know its dizzy – Let’s go into the details
R
G
B
GND

## Slide 7: Lighting system - KiCAD

## Slide 8: Lighting System KiCAD PCB Design

## Slide 9: Photoresistor - Fritzing
Resistor value changes as the incoming light level varies.
Pull down resistor of 10kΩ
Connected to channel 0 of MCP3008
MCP3008 operates through SPI0

## Slide 10: Photoresistor - KiCAD

## Slide 11: Photoresistor KiCAD PDB Design

## Slide 12: Linear Potentiometer - Fritzing
A varying resistor:
Depending on where you touch
Using current limiting resistors – 10k on Vcc and GND
100k as a pullup resistor on Collector
Closer to the collector, the smaller the resistor value
4 in total - Connected to channel 1-4 of MCP3008
Vcc
GND
Fritzing diagram taken from following:
https://github.com/sparkfun/Fritzing_Parts/blob/master/products/08680_softpot_membrane_potentiometer_50mm.fzpz
Collector

## Slide 13: Linear Potentiometer - KiCAD
Diagram Manually Created

## Slide 14: Linear Potentiometer KiCAD PCB Design

## Slide 15: Thank you
End of Document